## Slide 1
Tutorial 5: Wireless Control

## Slide 2
In today's tutorial we will work on controlling a motor using a remote
  Connect the DC motor and the IR Reciever to the arduino
  Determine what the IR Remote sends to the Arduino
    Adjust the Final Code to make sure it is looking for the right code
  Setup the proper code and upload it to the arduino, test out the functionality of the motor
There are a couple main steps

## Slide 3
1. Wiring of the Motor and the IR Reciever
Make sure that the motor is Connected to Pin 5, and the IR sensor is connected to pin 11
For the IR SENSOR:
G = Ground
R = 5V
Y = Signal – Pin 11

## Slide 4
Now we upload the code for testing the IR sensor
Test Vol -
Press the Vol - button and copy the output to Motor_test to where it require the value for VOL-
Test Vol+
Press the Vol + button and copy the output to Motor_test to where it require the value for VOL+
Open
Open Serial Monitor
Purpose
This code will run just the IR sensor and tell you what the Arduino Sees when you press a button
Upload
Upload the code IR_RECV

## Slide 5
Motor_Test
Make sure that everything is wired properly
Now once the code is uploaded, you can press the VOL+ and VOL- keys on the remote to make your motor spin faster and slower. Try it out
Open Serial Monitor, It will tell you what is being sent to the motor
*Be careful not to hold the button, quick presses
Compare your code to Finalcode file if there are any errors