## Slide 1: Tutorial 6

## Slide 2: Objectives
In our final Project, our cars will be controlled by a joystick sending messages through IR
So we will learn how to wire and code using a Joystick today.
As well we will also learn how to use the L293D Motor Controller

## Slide 3: Motor Drivers
Motor Drivers control which wire of the motor gets a voltage
There are three important pins in our layout
  The enable pin – To this pin we send what the speed of motor will be
  The inA pin, and inB pin- this controls which wire gets the positive and negative voltage
This way we can control which direction the motor spins

## Slide 4: Wiring

## Slide 5: Joysticks
Joysticks work by measuring how far in a particular direction the joystick is
From that we get a value and can control other systems
They read a value from 0-1023
We can set 0-512 for one direction and 513-1023 in another direction